## Slide 1: Exploring Energy Management

## Slide 2: What is Energy Management?
Energy management is doing more with the same amount of energy or less energy.
Energy management saves money and makes buildings more comfortable, healthy, and safe.

## Slide 3: Efficiency vs. Conservation
Efficiency
Energy efficiency involves the use of technology that requires less energy to perform the same function.
Focuses on the equipment or machinery being used
One example is installing LED light bulbs throughout the house
Conservation
Energy conservation includes any behavior that results in the use of less energy.
Focuses on the behavior of people
One example is using daylighting through windows rather than turning on the lights

## Slide 4: Benefits of Energy Management
Reduces consumption
Increases comfort & safety
Reduces pollution
Makes our economy stronger
Increases our energy security

## Slide 5: National ENERGY STAR® Program
Joint program of the U.S. Environmental Protection Agency and the U.S. Department of Energy
National symbol for energy efficiency
Products and/or buildings must meet certain standards to display label
For homes & businesses

## Slide 6: How Efficient are U.S. Schools?
Average annual energy bill to run America's schools: $6 billion
A typical school district with 3,000 students spends $400,000 on energy per year.
The least efficient schools use 3 times more energy than the best energy performers.
Top performing ENERGY STAR® labeled schools cost $0.40/square foot less to operate than the average schools.
Luckily, energy is a manageable expense.
Notes: Source: U.S. Dept. of Energy

## Slide 7: When we look for ways to save energy in a school, we must keep in mind:
The health and safety of the occupants.
Indoor air quality – adequate ventilation.
The comfort of the occupants.

## Slide 8: How Does Your School Use Energy?
  Building Envelope
  Heating, Ventilation and Air Conditioning (HVAC)
  Lighting
  Electric Appliances
  Energy System Components

## Slide 9: The Building Envelope
Any part of the building which creates a boundary between indoor and outdoor space.
  Walls
  Roofs
  Ceilings
  Doors
  Windows

## Slide 10: The Building Envelope
The envelope should limit:
  The amount of thermal energy conducting through.
  The amount of air that moves in and out of the building.

## Slide 11: Savings Opportunities: Building Envelope
Windows left open
Single-paned windows
Inadequate weatherstripping

## Slide 12: HVAC
Heating System (boiler, furnace)
Ventilation System
Air Conditioning (chillers)
Hot Water
Thermostats
Ducts and Pipes

## Slide 13: Building Automation System (BAS)
Temperature Sensor
Provides school personnel with real time energy and performance data to manage the building’s energy needs.

## Slide 14: Types of Lighting Found in Schools
Incandescent
Fluorescent
High Intensity Discharge (HID)
Light Emitting Diode (LED)

## Slide 15: Fluorescent

## Slide 16: Ballast
  Required for operation of fluorescent lamps.
  Provides initial arc to start lamp.
  Regulates current during operation.
  Two main types:
    magnetic
    electronic
Notes: Magnetic ballasts arc at a lower frequency than electronic ballasts. Electronic ballasts therefore allow for a more efficient light that flickers less.

## Slide 17: Compact Fluorescent
Miniature fluorescent with built in ballast
Ideal for replacement of incandescent lamps
Saves up to75% on energy use
Lasts 7-10 times longer than an incandescent
Low thermal energy output
Improved color rendition
Notes: Source: www.EnergyStar.gov

## Slide 18: Light Emitting Diodes (LEDs)
Energy Star bulbs rated at 25,000 hours.
Can use up to 50% less energy than a CFL.
Widespread use over the next 20 years could reduce lighting energy demand by 33%.
Currently more expensive to purchase compared to incandescent and CFLs.

## Slide 19: Comparing Light Bulbs Answer Key

## Slide 20: Electric Appliances in Schools
Electric Space Heaters
Air Conditioning
Electric Water Heaters
Refrigerators/Freezers
Lighting
Computers and Office Equipment

## Slide 21: Savings Opportunities: Electric Appliances
Monitors with Screen Savers, Power Saving Options Not Enabled

## Slide 22: Personal Computers
Set your computer to automatically go into STANDBY mode after 10 minutes.
To bring it back up, either move your mouse or hit the power button (depending on your machine).
Disable screensavers!
Enable Power Management Settings

## Slide 23: Saving with Vending Machines
Install timers
Unplug during vacations

## Slide 24: Plug Loads
Students count electrical devices
Students estimate number of hours per week device is used
Excel spreadsheet uses formulas to compute cost

## Slide 25: Student Energy Audit
Investigate your building and look for the following:
  Fluorescent light ballast type
  Light levels
  Humidity levels
  Temperature
  Electricity usage
Reporting Form (Before and After)

## Slide 26: Determining Ballast Type
A flicker checker is a small plastic top-like device used to identify ballast type. A gray scale pattern indicates an electronic ballast, while a checkerboard pattern indicates a magnetic ballast.

## Slide 27: Light Meter
A light meter measures the amount of light in a space in units of foot candles. Spaces that are overly lit may be using more energy than necessary.

## Slide 28: Hygrometer
A hygrometer measures relative humidity. Warmer air can hold more moisture, so if cold air is heated, it will feel very dry unless humidified.

## Slide 29: Digital Thermometer
The digital thermometer can be used to tell if a room is of the appropriate temperature, and compare how spaces may be infiltrated by thermal energy or moving air. Waterproof versions can also help check the temperature setting of your water heating system.

## Slide 30: Kill A Watt meter
This tool allows you to measure how much power (Watts) an electrical device uses at any given time. By changing the display, it will also measure kWh consumed over a period of time.

## Slide 31: Energy Efficiency: The Assessment

## Slide 32: Energy Efficiency: Take Action
What Makes a Campaign Effective?
Clearly defined message
Motivational components
Delivering message via multiple media
Persistence in delivering message
Awareness Campaign